## Slide 1: Resistance, Ohm’s Law
Physics 1161: Lecture 06
Homework, keep lots of digits!
Georg Ohm
Notes: 1

## Slide 2: Last Time
Capacitors C = Q/V -- definition
  Physical C = e0A/d
  Series 1/Ceq = 1/C1 + 1/C2
  Parallel Ceq = C1 + C2
  Energy U = 1/2 QV
Resistors R = V/I
  Physical R = r L/A
  Series Req = R1 + R2
  Parallel 1/Req = 1/R1 + 1/R2
  Power P = IV
Today

## Slide 3
Two cylindrical resistors are made from the same material. They are of equal length but one has twice the diameter of the other.
R1 > R2
R1 = R2
R1 < R2
2
1
Checkpoint Cylindrical Resistors 1

## Slide 4: Simple Circuit
Practice…
  Calculate I when e=24 Volts and R = 8 W
  Ohm’s Law: V =IR
R
e
I
I
Example
I = V/R
= 3 Amps

## Slide 5: Checkpoint Resistors in Series
Compare I1 the current through R1, with I10 the current through R10.
    I1 < I10
    I1 = I10
    I1 > I10
R1=1W
e0
R10=10W
Note: I is the same everywhere in this circuit!

## Slide 6: Compare V1 the voltage across R1, with V10 the voltage across R10.
R1=1W
e0
R10=10W
V1>V10
V1=V10
V1< V10

## Slide 7: Compare V1 the voltage across R1, with V10 the voltage across R10.
R1=1W
e0
R10=10W
V1 = I1 R1 = 1 x I
V10 = I10 R10 = 10 x I
V1>V10
V1=V10
V1< V10

## Slide 8: Practice: Resistors in Series
Calculate the voltage across each resistor if the battery has potential V0= 22 volts.
  R12 = R1 + R2
  V12 = V1 + V2
  I12 = I1 = I2
= 11 W
R12
e0
= V0 = 22 Volts
= V12/R12 = 2 Amps
Expand:
  V1 = I1R1
  V2 = I2R2
= 2 x 1 = 2 Volts
= 2 x 10 = 20 Volts
R1=1W
e0
R2=10W
Check: V1 + V2 = V12 ?
Simplify (R1 and R2 in series):
R1=1W
e0
R2=10W
Example
YES!

## Slide 9: Checkpoint 2 Light Bulbs
What happens to the current through R2 when the switch is closed?
Increases
Remains Same
Decreases
V2 = ε = I2R2

## Slide 10: What happens to the current through the battery when the switch is closed?
Increases
Remains Same
Decreases

## Slide 11: What happens to the current through the battery when the switch is closed?
Increases
Remains Same
Decreases

## Slide 12: Practice: Resistors in Parallel
Determine the current through the battery.
Let E = 60 Volts, R2 = 20 W and R3=30 W.
  1/R23 = 1/R2 + 1/R3
  V23 = V2 = V3
  I23 = I2 + I3
R2
R3
e
R23
e
Simplify: R2 and R3 are in parallel
Example
R23 = 12 W
= 60 Volts
= V23 /R23 = 5 Amps

## Slide 13: Why is it dangerous to use one power strip to plug in and use simultaneously your microwave, coffee pot, toaster, and hair dryer (current through hair dryer is 10 A)?
The resistance of the kitchen circuit is too high.
The voltage across the kitchen circuit is too high.
The current in the kitchen circuit is too high.

## Slide 14: Why is it dangerous to use one power strip to plug in and use simultaneously your microwave, coffee pot, toaster, and hair dryer (current through hair dryer is 10 A)?
The resistance of the kitchen circuit is too high.
The voltage across the kitchen circuit is too high.
The current in the kitchen circuit is too high.

## Slide 15: Checkpoint Comparison of Resistance
Which configuration has the smallest resistance?
1
2
3
1
2
3
Which configuration has the largest resistance?
2
R 2R R/2

## Slide 16: Parallel + Series Tests
Resistors R1 and R2 are in series if and only if R1 and R2 are connected with a single wire (NO branches)
Resistors R1 and R2 are in parallel if and only if you can make a loop that has ONLY R1 and R2
Same rules apply to capacitors!!

## Slide 17
Voltage
Current
Resistance
Series
Parallel
Summary
Different for each resistor.
Vtotal = V1 + V2
Increases
Req = R1 + R2
Same for each resistor
Itotal = I1 = I2
Same for each resistor.
Vtotal = V1 = V2
Decreases
1/Req = 1/R1 + 1/R2
Wiring
Each resistor on the same wire.
Each resistor on a different wire.
Different for each resistor
Itotal = I1 + I2
R1
R2
R1
R2