## Slide 1: Circuits

## Slide 2: Preflight 9-1
Two resistors of very different value are connected in parallel. Will the resistance of the pair be closer to the value of the larger resistor or the smaller one?
  the larger resistor __%
  the smaller resistor
Car Headlights are connected
Connect 4 equal resistors so their Req is R
__%
In parallel

## Slide 3: As more identical resistors R are added to the parallel circuit shown here, the total resistance between points P and Q
increases
remains the same
decreases
Q

## Slide 4: As more identical resistors R are added to the parallel circuit shown here, the total resistance between points P and Q
increases
remains the same
decreases
Q

## Slide 5: Charge flows through a light bulb. Suppose a wire is connected across the bulb as shown. When the wire is connected,
all the charge continues to flow through the bulb.
half the charge flows through the wire; the other half continues through the bulb.
all the charge flows through the wire.
None of the above

## Slide 6: Charge flows through a light bulb. Suppose a wire is connected across the bulb as shown. When the wire is connected,
all the charge continues to flow through the bulb.
half the charge flows through the wire; the other half continues through the bulb.
all the charge flows through the wire.
None of the above

## Slide 7: Power
Power is the rate at which energy is used or at which work is done
P = IV
Units:

## Slide 8: Practice: Resistors in Series
Calculate the power provided by the battery if the battery emf is 22 volts. Calculate the power dissipated by each resistor
  R12 = R1 + R2
  I12 = V/R12
  P = IV
= 11 W
R12
e0
= I12 = 2 Amps
= 2 A*22 V = 44 W
Expand:
  V1 = I1R1
  P = IV
  V2 = I2R2
  P = IV
= 2 x 1 = 2 Volts
=2 A * 2 V = 4 W
= 2 x 10 = 20 Volts
= 2 A * 20 V = 40 W
R1=1W
e0
R2=10W
Check: P1 + P2 = Pbattery ?
Simplify (R1 and R2 in series):
R1=1W
e0
R2=10W
Example

## Slide 9: Practice: Resistors in Parallel
Determine the current through the battery.
Let  = 60 Volts, R2 = 20 W and R3=30 W.
  1/R23 = 1/R2 + 1/R3
  V23 = V2 = V3
  I23 = I2 + I3
R2
R3
e
R23
e
R23 = 12 W
= 60 Volts
= V23 /R23 = 5 Amps
Simplify: R2 and R3 are in parallel
Example

## Slide 10: Practice: Resistors in Parallel
What is the power delivered by the battery and what is the power dissipated by each resistor.
Let  = 60 Volts, R2 = 20 W and R3=30 W.
  P = I*V
  P2 = I2 V2
  P3 = I3 V3
R2
R3
e
R23
e
= (5 A)(60 V) = 300 W
= (3 A)(60 V) = 180 W
= (2 A)(60V) = 120 W
Calculate IV for the battery.
Example

## Slide 11: Try it!
R1
R2
R3
Calculate current through each resistor.
R1 = 10 W, R2 = 20 W, R3 = 30 W, e=44 V
Simplify: R2 and R3 are in parallel
  1/R23 = 1/R2 + 1/R3
  V23 = V2 = V3
  I23 = I2 + I3
Simplify: R1 and R23 are in series
  R123 = R1 + R23
  V123 = V1 + V23= e
  I123 = I1 = I23 = Ibattery
: R23 = 12 W
: R123 = 22 W
R123
e
R1
R23
e
e
: I123 = 44 V/22 W = 2 A
Power delivered by battery?
P=IV = 244 = 88W
Example

## Slide 12: Try it! (cont.)
R1
R2
R3
Calculate current through each resistor.
R1 = 10 W, R2 = 20 W, R3 = 30 W, e=44 V
Expand: R2 and R3 are in parallel
  1/R23 = 1/R2 + 1/R3
  V23 = V2 = V3
  I23 = I2 + I3
Expand: R1 and R23 are in series
  R123 = R1 + R23
  V123 = V1 + V23= e
  I123 = I1 = I23 = Ibattery
R123
e
R1
R23
e
e
: I23 = 2 A
: V23 = I23 R23 = 24 V
I2 = V2/R2 =24/20=1.2A
I3 = V3/R3 =24/30=0.8A
Example

## Slide 13: If the 4 light bulbs in the figure are identical, which circuit puts out more light?
I
They emit the same amount of light
II
I
II

## Slide 14: If the 4 light bulbs in the figure are identical, which circuit puts out more light?
I
They emit the same amount of light
II
I
II