## Slide 1: Physics 1161: Lecture 8 Kirchhoff’s Laws

## Slide 2: Kirchhoff’s Rules
Kirchhoff’s Junction Rule:
  Current going in equals current coming out.
Kirchhoff’s Loop Rule:
  Sum of voltage changes around a loop is zero.

## Slide 5: Using Kirchhoff’s Rules
Label all currents
(3)Choose loop and direction
  Choose any direction
  You will need one less loop than
  unknown currents
(4) Write down voltage changes
Be careful about signs
For batteries – voltage change is positive when summing from negative to positive
For resistors – voltage change is negative when summing in the direction of the current
R4
I1
I3
I2
I4
R1
1
R2
R3
 2
3
R5
A
B
(2) Write down junction equation
Iin = Iout
I5
Notes: Have students label I5, since it isn’t shown in their drawing

## Slide 6: Loop Rule Practice
R1=5 W
I
e1= 50V
R2=15 W
e2= 10V
A
B
Find I:
Example
Notes: Ask if R1 and R2 are in series, parallel.

## Slide 7: Loop Rule Practice
R1=5 W
I
+e1 - IR1 - e2 - IR2 = 0
+50 - 5 I - 10 - 15 I = 0
I = +2 Amps
e1= 50V
R2=15 W
e2= 10V
A
B
Find I:
Example
Label currents
Choose loop
Write KLR

## Slide 8: Resistors R1 and R2 are
In parallel
In series
neither
I1
R1=10 W
R2=10 W
E1 = 10 V
IB
E2 = 5 V
I2
+
-

## Slide 9: Resistors R1 and R2 are
In parallel
In series
neither
I1
R1=10 W
R2=10 W
E1 = 10 V
IB
E2 = 5 V
I2
+
-
Definition of parallel:
Two elements are in parallel if (and only if) you can make a loop that contains only those two elements.
Upper loop contains R1 and R2 but also E2.

## Slide 10: Checkpoint 1
1) I1 = 0.5 A 2) I1 = 1.0 A 3) I1 = 1.5 A
E1 - I1R1 = 0
Calculate the current through resistor 1.
 I1 = E1 /R1 = 1A
Notes: Note that nothing is in series or in parallel!

## Slide 11: How would I1 change if the switch was opened?
E1 = 10 V
IB
R=10 W
I1
R=10 W
I2
E2 = 5 V
Increase
No change
Decrease

## Slide 12: How would I1 change if the switch was opened?
E1 = 10 V
IB
R=10 W
I1
R=10 W
I2
E2 = 5 V
Increase
No change
Decrease

## Slide 13: Checkpoint 2
I2 = 0.5 A
I2 = 1.0 A
I2 = 1.5 A
E1 - E2 - I2R2 = 0
 I2 = 0.5A
Calculate the current through resistor 2.

## Slide 14: Checkpoint 2
R=10 W
E1 = 10 V
IB
I1
E2 = 5 V
R=10 W
I2
-
+
+
-
+E1 - E2 + I2R = 0 Note the sign change from last slide
 I2 = -0.5A Answer has same magnitude as before but opposite sign. That means current goes to the left, as we found before.
How do I know the direction of I2?
It doesn’t matter. Choose whatever direction
you like. Then solve the equations to find I2.
If the result is positive, then your initial guess
was correct. If result is negative, then actual
direction is opposite to your initial guess.
Work through preflight with opposite
sign for I2?

## Slide 15: Kirchhoff’s Junction Rule
Current Entering = Current Leaving
I1
I2
I3
I1 = I2 + I3
1) IB = 0.5 A 2) IB = 1.0 A 3) IB = 1.5 A
IB = I1 + I2 = 1.5 A
R=10 W
E1 = 10 V
IB
I1
E = 5 V
R=10 W
I2
+
-
Checkpoint 3
“The first two can be calculated using V=IR because the voltage and resistance is given, and the current through E1 can be calculated with the help of Kirchhoff's Junction rule, that states whatever current flows into the junction must flow out. So I1 and I2 are added together.”

## Slide 16: Kirchhoff’s Laws
(1) Label all currents
  Choose any direction
Write down the junction equation
  Iin = Iout
Choose loop and direction
  Your choice!
Write down voltage changes
Follow any loops
Solve the equations by substitution or combination .
R4
R1
E1
R2
R3
E2
E3
I1
I3
I2
I4
R5
A
B

## Slide 17: You try it!
In the circuit below you are given e1, e2, R1, R2 and R3. Find I1, I2 and I3.
R1
R2
R3
I1
I3
I2
+
-
e1
e2
+
-
Example
Notes: 1) This will be given on the exam. Comment on 1 equation 2 unknowns. 2 eqs 3 unknowns finally 3 and 3

## Slide 18: You try it!
R1
R2
R3
I1
I3
I2
+
-
Loop 1: +e1- I1R1 + I2R2 = 0
Label all currents (Choose any direction)
3. Choose loop and direction (Your choice!)
Write down voltage changes
Loop 2:
e1
Node: I1 + I2 = I3
e2
3 Equations, 3 unknowns the rest is math!
In the circuit below you are given e1, e2, R1, R2 and R3. Find I1, I2 and I3.
Loop 1
Loop 2

+
-


- I2R2 - I3R3 - e2 = 0


Example
2. Write down junction equation

## Slide 19: Let’s put in actual numbers
In the circuit below you are given e1, e2, R1, R2 and R3. Find I1, I2 and I3.
2
5
10
10
I1
I3
I2
+
-
20
+
-
Example
1. junction: I3=I1+I2
2. left loop: 20 - 5I1+10I2 = 0
3. right loop: -2 - 10I2 - 10I3 = 0
solution: substitute Eq.1 for I3 in Eq. 3:
rearrange: -10I1 - 20I2 = 2
rearrange Eq. 2: 5I1-10I2 = 20
Now we have 2 eq., 2 unknowns. Continue on next slide

## Slide 20
-10I1-20I2 = 2
2*(5I1 - 10I2 = 20) = 10I1 – 20I2 = 40
Now we have 2 eq., 2 unknowns.
Add the equations together:
-40I2 = 42 I2 = -1.05 A
note that this means direction of I2 is opposite to that shown on the previous slide
Plug into left loop equation:
5I1 -10*(-1.05) = 20
I1=1.90 A
Use junction equation (eq. 1 from previous page)
I3=I1+I2 = 1.90-1.05
I3 = 0.85 A